## Slide 1: Yeti设备驱动列表

## Slide 2: LCD
DSI interface
  Drivers/gpu/drm/i915/intel_dsi.c
Panel driver
  Drivers/gpu/drm/i915/intel_dsi_nt35523_vid.c
  /sys/class/graphics/fb0
Backlight
  Hardware/intel/lights
  /sys/class/backlight/intel-backlight
Lcd effect
  Drivers/gpu/drm/i915/lenovo_lcd_panel.c
  /sys/class/lcd_class/lcd0

## Slide 3: Power按键
/dev/input/event6
Name:gpio-lesskey
Value:ev_key;ev_syn
  /sys/bus/platform/devices/gpio-lesskey.1.auto/

## Slide 4: 音量键
/dev/input/event7
Name:gpio-keys
Value:ev_key;ev_syn
  /sys/bus/platform/devices/gpio-keys.2.auto/

## Slide 5: Smtpad(鼠标功能)
Drivers/input/touchscreen/smtpad/
DEVICE NODE
  /dev/input/event5
Name:lenovo-smartpad_touch
Value:ev_key;ev_syn

## Slide 6: keyPad(物理按键）笔转换键盘灯
驱动
  Drivers/input/keyboard/gpio_keys.c
  Drivers/input/misc/soc_button_array.c
  Drivers/input/keyboard/acpi-gpiobtn.c[N not have]
Device node
  /sys/bus/platform/devices/gpio-keys.2.auto/
  /sys/class/input/input7
  /sys/bus/platform/devices/gpio-lesskey.1.auto/
  /sys/class/input/input6
  /sys/bus/pnp/devices/00:10
  Report coordinate and key data by input sub-system
/dev/input/event6
Name:gpio-lesskey
Value:ev_key;ev_syn
Notes: 笔转换灯跟电源键event号一样，但是报值的类型不同，一个是key_power,一个是key_kdbinputassist_p

## Slide 7: Main TP(触屏)
Firmware /kernel/cht/firmware/
driver
  drivers\input\touchscreen\ist940e
  Arch/x86/platform/intel/device_libs/Platform_ist940e.c
  Include/linux/input/ist520e.h
Device node
  /sys/bus/i2c/devices/i2c-5/5-006c
  /sys/class/input/input3
  Access TP chip by I2C bus
  Report coordinate and key data by input sub-system
/dev/input/event3
Name:hideep
Value:ev_key;ev_syn;ev_abs

## Slide 8: Sub-TP(touch-keyboard)
    driver
    drivers\input\touchscreen\Gt9xx
    Arch/x86/platform/intel/device_libs/Platform_gt9xx.c
Device node
  /sys/bus/i2c/devices/1-0014
  /sys/class/input/input4
  Access TP CHIP by I2C bus
  Report coordinate and key data by input sub-system
/dev/input/event4[坐标值]
Name:lenovo-smartpad_ts
Value:ev_abs;ev_syn
/dev/input/event10[转换后的键值]
Name:flat_keyboard
Value:ev_key;ev_syn
Notes: 这个驱动的数据流不是单纯的走input子系统。中间有个deamon叫做oskd，对driver数据进行修改再向上传输[将xy的raw数据转换成keyboard的raw数据，放到event10的flatkeyboard里面，然后走正常的input流程][坐标扫描码转按键扫描码，再走input子系统转按键码]

## Slide 9: EMR（画板）
Firmware
device/lenovo/common/wacom
Driver
    arch\x86\platform\intel-mid\device_libs\ platform_wacom.c
    drivers\input\touchscreen\wacom_i2c.c
    include\linux\input\ wacom.h
UPDATA firmware
vendor/lenovo/common/common.mk
vendor/lenovo/wacom/
Device node
  /sys/bus/i2c/devices/3-0009
  /sys/class/input/input8
  Access EMR HW by I2C bus
  Report coordinate and key data by input sub-system
/dev/input/event8
Name:wacom_i2c_digitizer
Value:ev_key,ev_abs.ev_syn

## Slide 10: SAR Sensor 感应物体，人
Driver
  drivers\input\misc\smtc
  arch\x86\platform\intel-mid\device_libs\ platform_sx9310.c
  Include\linux\input\smtc\
Device node
  /sys/bus/i2c/devices/1-0028
  /sys/bus/i2c/devices/3-0028[N not have]
    &dev_attr_calibrate.attr,
    &dev_attr_reg.attr,
    &dev_attr_status.attr,[0.1.2.3]
    &dev_attr_enable.attr,
    &dev_attr_sarconfig.attr,
  Store/get 函数没有用锁保护，需添加

## Slide 11: Hall Sensor 感应合上，分开
driver
  Drivers\switch\
  arch\x86\platform\intel-mid\device_libs\platform_hall.c
  Include\linux\switch_hall.c
Device node
  /sys/class/switch2/hall
  /sys/class/switch2/sec_hall
    State
    Uevent(obj_changed)

## Slide 12: Other sensors attached to ISH
ALS
Ecompass
ACC
Hinge
Tool
sensorhub_client –c1 –tACCEL –r10 –d0[从hub拿到的数据]
Dumpsys sensorservice[从hal拿到的数据]

## Slide 13: Vibrators
driver
  drivers\input\misc\drv2604l_haptics.c
  arch\x86\platform\intel-mid\device_libs\ platform_haptics_2604l.c
  Include\linux\haptics\drv2604l.h
  Drivers\input\misc\touchsensor\
  Hardware/libhardware/modules/vibrator/
  external/touchsense/
Firmware
- firmware\drv2604.bin.ihex
Device node
  /sys/bus/i2c/devices/0-005a
  /sys/bus/i2c/devices/3-005a
  /sys/class/drv2604L/drv2604L_0
  /sys/class/drv2604L/drv2604L_1
    Fops-open,close,write
  /sys/class/switch2/haptics_0
  /sys/class/switch2/haptics_1
    state
  /sys/class/timed_output/vibrator_0
  /sys/class/timed_output/vibrator_1
    vibrator_get_time
    vibrator_enable

## Slide 14: LED-keyboard
driver
  /drivers/leds/leds-tps61163a.c
  arch\x86\platform\intel-mid\device_libs\ platform_tps61163a.c
  Include/linux/leds_pwm.h
Device node
  /sys/class/leds/keyboard-led
  Framework to ctrl this LED when switch EMR and keyboard mode

## Slide 15: LED-charging
PMIC provide,also need to merge it

## Slide 16: Intel-sensor-hub
MCU driver:
Driver/misc/intel-ish/ipc.c
Driver/misc/intel-ish/ipc-ish.c[probe here]
Vendor/intel/hardware/ish-sensors
Vendor/intel/hardware/libsensorhub

## Slide 17: LED-button

## Slide 18: camera
Driver
  /drivers/external_drivers/camera/drivers/media/i2c/ov8858.c
  /drivers/external_drivers/camera/drivers/media/i2c/ov2740.c
  Device info from ACPI
Device node
  sys/bus/i2c/devices/i2c-2/device/i2c-2/i2c-INT33BE:00 --〉OV2740
  sys/bus/i2c/devices/i2c-2/device/i2c-2/i2c-INT33FB:00 --〉OV8858
  V4L2 device , data / control pipeline by IOCTL

## Slide 19: Other devices
Audio
Camera
Charger&battery
PMIC

## Slide 20
先把设备文件加载了一遍
后面才加载驱动文件